General Design Information for Construction in Berkeley County (As of January 1, 2023)

- The International Building Code (IBC) 2021 Edition*

- The International Residential Code (IRC) 2021 Edition for One- and Two-Family Dwellings and Townhouses*

- The International Mechanical Code (IMC) 2021 Edition*

- The International Energy Conversation Code (IECC) 2009 Edition*

- The International Fire Code (IFC) 2021 Edition*

- The International Existing Building Code (IEBC) 2021 Edition*

- The International Plumbing Code (IPC) 2021 Edition*

- The International Fuel Gas Code (IFGC) 2021 Edition*

- The National Electrical Code (NEC) 2020 Edition*

- ICC A117.1 (ANSI) 2017 Edition*

- The 8th Edition of the Manual J

*All codes adopted above are with South Carolina Modifications.

| GROUND SNOW LOAD | WIND DESIGN | SEISMIC DESIGN CATGEORY | SUBJECT TO DAMAGE FROM | Winter Design Temperature | Ice Breakers Underlayment Required | Flood Hazard | Air Freezing Index | Mean Annual Temperature |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Speed (mph) | Topographic effects | Special Wind Region | Wind Borne Debris Region |  | Weathering | Frost Line Depth | Termite |  |  |  |  |  |
| 5 | 133–150 *See Note | No | No | **See Note | Residential D2 Commercial D | Modest | 12” | Moderate to Heavy | 32 | No | ***See Note | 30 | 64.8 |

*Wind Speed:

Residential Construction: will be based off the SC LLR Maps that are available at https://llr.sc.gov/bcc/PDFfiles/WSMaps/Berkeley%2015(Mays).pdf

Commercial Construction: will be based on the ATC Hazards by Location website available at: https://hazards.atcouncil.org/#/

Please be advised that the Building Official has the authority to determine the wind speed for each location.

**Wind Borne Debris Region. Please refer to SC LLR Maps available at https://llr.sc.gov/bcc/PDFfiles/WSMaps/Berkeley%2015(Mays).pdf

***Flood Hazard: Please refer to the FEMA website for Hazardous Flood Locations.

| Manual J Design Criteria Location: Charleston Intl AP, SC, US |
| --- |
| Elevation | Latitude | Winter Heating | Summer Cooling | Altitude Correction Factor | Indoor Design Temperature | Design Temperature Cooling | Heating Temperature Difference |
| 49 | 33 | 28 | 92 | 1.0 (405) | 75 | 75 | 40 |
| Cooling Temperature Difference | Wind Velocity heating | Wind Velocity Cooling | Coincident Wet bulb | Daily Range | Winter Humidity | Summer Humidity |  |
| 17 | 15 | 7.5 | 77 | 16 (M) | 50 | 50 |  |

# Text boxes

BERKELEY COUNTY

BUILDING AND CODE ENFORCEMENT

Henry Jackson

Chief Building Official